# ATLAS Toroid History

Updated: 28 November 2006 (Roger Ruber)

Information from:

- Elwyn Baynham (RAL)

- Laurent Chevalier (CEA)

- Antoine Daël (CEA)

- Herman ten Kate (CERN)

CERN library:

- ATL-TECH-92-003, ATL-TECH-92-004 (EAGLE)

- ATL-TECH-93-008 (ASCOT)

- ROM-NI-999 (ASCOT): S. Petrarca et al. (1992)

- Evian-les-Bains (1992) Proceedings of the General Meeting on LHC Physics & Detectors

## 1980s: Experiment Proposals for LEP

An experiment with a toroidal magnet is proposed (but rejected) for LEP.

Marc Virchaux (NA4, deep-inelastic muon scattering) is the driving force behind the idea for a muon spectrometer with an air-core toroid.

## 1992: Experiment Proposals for LHC

### EAGLE (Peter Jenni):

Inner tracking detector in a 2 T solenoidal field

- inner detector radius 1.1 m, length 8 m

- thin superconducting solenoid (~1.0 X0, Δr = ~0.22 m)

- common cryostat for solenoid and liquid argon calorimeter

Accordion type liquid argon calorimeter

Hermetic hadron calorimeter (fibres or tiles)

Warm iron toroid muon spectrometer

- 2-4 m thick

- inner radius 4.6 m, length 14.7 m

- outer radius 9.18 m, length 27.120 m

Total weight 26,400 t (estimated)

### ASCOT

central tracking detector

1.5 T solenoid

Liquid argon calorimeter

Muon spectrometer with 12 coils toroid (compare to 6 coils toroid for CLAS at CEBAF)

- Superconducting iron core end-cap toroids

  - twin toroid (2 behind each other with detectors in between)

  - radius 1.0 – 4.65 m, length 4.8 m

  - field at iron 2.45 – 3.72 T at 23.8 kA

- Superconducting air core barrel toroid

  - coil cryostats 26 x 5 m2

  - pancake shaped cryostat with sliced hole for detectors

  - 10 cold voussoir rings (inner support ring)

  - 10 warm strud rings (outer support ring)

  - overall support from the mid-plane, connected through the cryostat (cold mass) with sliding interface

  - inner free radius 5 m (outer radius 9.9 m)

  - peak field at conductor 3.5 T at 20 kA, 26x106 Aturns

Total weight 10,500 t (estimated)

### ATLAS

Combination of EAGLE + ASCOT, due to similarities in design.

Interface region at 5 m radius:

- EAGLE inner detector + calorimeters

- ASCOT muon spectrometer with air core toroid

## 1994-1996: ATLAS pre-design studies

Barrel Toroid (CEA)

- cold voussoirs

- connection voussoirs at ribs

End-Cap Toroid (RAL)

- single cryostat

Solenoid (KEK)

- thin-walled (0.66 X0) by using reinforced aluminium stabilizer

Design is considered too expensive. Costs for ATLAS should be equal to CMS.

Re-design:

- from 12 to 8 coils

- total ampere-turns 10% down

- barrel toroid gets warm support structure

  - warm voussoir

  - interface by titanium tie rods connected in between the cold ribs

  - tie rods can bend following the contraction of the coil during cool down

  - main support does no longer require warm to cold interface

  - main support feet moved from mid-plane to the bottom

- barrel toroid gets circular cryostats
(simpler, cheaper and more space for the detector)

## 1996 – 1999: Final design adjustments

Toroids:

- construction model coil B0 to study warm support design solutions (with help of LASA)

- same superconducting Rutherford cable for ECT and BT

- ECT and BT connected in series