# Sector Processor Core Logic Interface

### Alex Madorsky, UF/Physics

09/06/07

## Inputs

### me1a – me1f

Six track stub inputs from station 1

| Bits | Name | Description |
| --- | --- | --- |
| 11:0 | Phi | Phi of the track stub |
| 18:12 | Eta | Eta of the track stub |
| 22:19 | Q | Quality of the track stub |
| 26:23 | CSCid | Chamber number this track stub belongs to |
| 27 | Valid | 1 if this track stub is valid |

### me2a – me2c, me3a – me3c, me4a – me4c

Track stub inputs from stations 2,3,4, three stubs from each.

| Bits | Name | Description |
| --- | --- | --- |
| 11:0 | Phi | Phi of the track stub |
| 18:12 | Eta | Eta of the track stub |
| 22:19 | Q | Quality of the track stub |
| 26:23 | reserved | These bits are reserved |
| 27 | Valid | 1 if this track stub is valid |

### mb1a – mb1b

Two track stub inputs from drift tube trigger system. Data on these inputs can be serialized by DT trigger system (see FL flag below)

| Bits | Name | Description |
| --- | --- | --- |
| 11:0 | Phi | Phi of the track stub |
| 14:12 | Q | Quality of the track stub |
| 15 | FL | FL is set to 1 if this track stub belongs to the previous BX |

### mneta0-7, mxeta0-7, etawn0-5

| Name | Description |
| --- | --- |
| Mneta | Minimum eta, 8 values |
| Mxeta | Maximum eta, 8 values |
| Etawn | Eta window, 6 values |

Default values for these parameters are shown below. These values should be applied to these inputs upon power-up or reset signal. All numbers are decimal:

mneta0 = 22;

mneta1 = 22;

mneta2 = 14;

mneta3 = 14;

mneta4 = 14;

mneta5 = 10;

mneta6 = 10;

mneta7 = 10;

mxeta0 = 127;

mxeta1 = 127;

mxeta2 = 127;

mxeta3 = 127;

mxeta4 = 127;

mxeta5 = 24;

mxeta6 = 24;

mxeta7 = 24;

etawn0 = 4;

etawn1 = 4;

etawn2 = 4;

etawn3 = 4;

etawn4 = 4;

etawn5 = 4;

### mindphi

Minimum phi difference for track cancellation logic, default = 120

### mindeta_acc

Minimum eta difference for accelerator tracks, default = 4

### maxdeta_acc

Maximum eta difference for accelerator tracks, default = 16

### maxdphi_acc

Maximum phi difference for accelerator tracks, default = 64

### control

Control input. Used to turn on/off various features in the core.

| Bits | Name | Description | Default | Range |
| --- | --- | --- | --- | --- |
| 0 | reserved |  | 0 |  |
| 3:1 | BXA_depth | Depth of BXA history | 2 | 0-2 |
| 4 | Allow ALCT-only | Allow ALCT-only track segments | 0 |  |
| 5 | Allow CLCT-only | Allow CLCT-only track segments | 0 |  |
| 6 | reserved |  | 0 |  |
| 8:7 | Pretrigger | Number of track segments to pre-trigger | 2 | 1-3 |
| 15:9 | reserved |  | 0 |  |

### clk

Clock input, 40 MHz.

## Outputs

### pHp, pMp, pLp

Parameters of the tracks found by the track finder on each clock cycle. pHp is the highest quality track, pLp is the lowest.

| Bits | Name | Description |
| --- | --- | --- |
| 4:0 | eta | Eta of the track that was found |
| 8:5 | mode | Mode parameter |
| 9 | charge | Charge of the particle |
| 21:10 | dphi | Delta Phi |
| 22 | sign | Sign |
| 27:23 | phi | Phi of the track that was found |
| 28 | FR | Front/rear flag – tells if ME1 chamber is in front of rear |

PT assignment lookup memory address should be constructed as shown below:

Addr = {FR, sign, mode, eta[4:1], dphi};

### idHp, idMp, idLp

Numbers of the track stubs which resulted into track found by the logic. idHp shows the track stubs for pHp output, idMp for pMp, and idLp for pLp. All numbers start from 1. 0 means that no track stub from this station participated in the decision.

| Bits | Name | Description | Range |
| --- | --- | --- | --- |
| 2:0 | Id1 | Number of track stub from station 1 | 1-6 |
| 5:3 | Bxd1 | Track stub from station 1 delay by BXA | 0-2 |
| 8:6 | Id2 | Number of track stub from station 2 | 1-3 |
| 11:9 | Bxd2 | Track stub from station 2 delay by BXA | 0-2 |
| 14:12 | Id3 | Number of track stub from station 3 | 1-3 |
| 17:15 | Bxd3 | Track stub from station 3 delay by BXA | 0-2 |
| 20:18 | Id4 | Number of track stub from station 4 | 1-3 |
| 23:21 | Bxd4 | Track stub from station 4 delay by BXA | 0-2 |
| 26:24 | Idb1 | Number of track stub from DT station 1 | 1-4 |
| 29:27 | Bxdb1 | Track stub from DT station 1 delay by BXA | 0-2 |
| 32:30 | Idb2 | Number of track stub from DT station 2 (kept for compatibility with older model, should be always 0) | 1-4 |
| 35:33 | Bxdb2 | Track stub from DT station 2 delay by BXA | 0-2 |

### date

Shows the date when this version of the core was generated from VPP model.

| Bits | Name | Description |
| --- | --- | --- |
| 0:6 | Year | Year – 2000 |
| 11:7 | Day | Day |
| 15:12 | Month | Month |