# DIRAC status report

10/30/2012 12:07:53 PM

I. RUN 2012

1. The strength of magnetic field decreased by less than 0.5 % during 4 months work with the proton beam intensity of 3·1011 protons/spill and with 100 µm Be target (see Fig. 1-9).

2. The beam position on the target in Y (vertical) direction is deflected from the optimal position by less than 0.5 mm during the 2012 run (see Fig. 10). The optimal distance between proton beam axis and the edge of Pt foil equals 7.5 mm. A 0.5 mm reduction of this distance excludes interaction of the proton beam halo with Pt foil edge.

3. The number of spills delivered to DIRAC from July to October 18 is 6.14×105. If the DIRAC has 3 spills/supercycle thereafter, the expected total number of spills during the 2012 run will be around 7.3×105.

4. The data from July up to September 28 (5.05×105 spills) is processed at the present time. The full number of A2π (NA=5700±500) was obtained from the Coulomb π+π– pairs analysis. In accordance with M.C. simulation the corresponding number of atomic pairs after long-lived A2π breaking in Pt foil will be na=130±12. For the total number of spills 7.3×105 in the 2012 run the expected signal from the atomic pairs will be at the level of more than 6σ.

II. RUN 2011

1. All experimental data was preselected and ntuples were prepared.

2. Multiple scattering measurements.

Events with only one track in each projection are selected in the present analysis.

For these events, analysis for Ni targets with 100 µm and 150 µm thickness (see Fig. 11, 12) was performed. The preliminary precision of multiple scattering angle measurement for each target is 0.7 %. This is better than 1 % precision in the 2003 run. In the 2003 run all events were used for the analysis. The precision of multiple scattering angle measurement in the 2011 run with full statistics is expected to be better than 0.5 % for each target. This measurement continues in the 2012 run.

III. ππ  atoms (RUNS 2008, 2009, 2010)

The analysis of the systematic errors is performed on the 2008 data after e+e– background subtraction. The number of atomic pairs is obtained for the events with low level of background in SFD, using distributions of pairs over Q, Ql and Ql-Qt. The difference between number of atomic pairs was due to the systematic error related to the new SFD planes. After reduction of the systematic error, the number of atomic pairs are 3455±163 (Q), 4059±270 (Ql) (see Fig.13,14) and 3601±162 (Ql–Qt). The atom breakup probability Pbr=(45.6±3.4)%(Ql) is the same as Pbr=(44.6±0.9)% obtained in the 2001-2003 runs. The way to decrease the systematic error is known. The total number of atomic pairs detected in the 2008-2010 runs will exceed 21000.

IV. π–K+ and π+K- atoms (RUNS 2008, 2009, 2010)

The multiplicity in all detectors for ππ and πK-triggers is the same.

Therefore suppression of the systematic error applied in the ππ atom analysis can be also used in the πK atom analysis. The preliminary results of analysis of the produced πK atoms and πK atomic pairs are expected to be ready in April 2013. This analysis will take into account the non point-like π and K meson production. The total number of πK atoms detected in the 2008-2010 runs will be around 600.

V. The new ionization hodoscope

The existing ionization hodoscope (IH) has 4 planes with S=108x108 mm2 assembled from 16 slabs with thickness of 1 mm.

Each slab is connected to PM photocathode by lucite light guide.

Each plane of the new IH has 32 slabs.

The increased granularity allows to decrease the signal overlapping and dead time of electronics. The new IH is presented in the Fig. 15-17.

This detector is installed in the beam and will be investigated during October 2012.

VI. DIRAC dismantle

The DIRAC setup dismantle will be finished before June 2013 in accordance with the plan prepared by CERN and DIRAC collaboration.

Figure 1

Figure 2

Figure 3

Figure 4

Figure 5

Figure 6

Figure 7

Figure 8

Figure 9

Figure 10. Beam 2012 (X and Y positions)

Figure 11. Run 2011. Analysis of multiple scattering in Ni (100 µm). Events with only one track in each projection were analyzed. δθ/θ y 0.7 %. This value is expected to be less than 0.5 % after including full statistics into the analysis.

Figure 12. Run 2011. Analysis of multiple scattering in Ni (150 µm). Events with only one track in each projection were analyzed. δθ/θ y 0.7 %. This value is expected to be less than 0.5 % after including full statistics into the analysis.

Figure 13

Figure 14

Figure 15. New IH outside

Figure 16. Scintillator plane of new IH

Figure 17. Clear fiber to scintillators