## Slide 1: Discussion on Studies at Test Stands
Roger Ruber
Uppsala University

## Slide 2: RF Generation and Distribution System
200 cavities (352 + 704 MHz)
  200 RF systems: modulator, klystron, distribution, controls
  5 MW beam → 20 MW RF, (losses and LLRF overhead)
R&D objectives
  energy efficiency and operational costs reductions
  produce technical design, with cost estimate, to start tendering
Notes: 2

## Slide 3: Test Stand Objectives
Prototype baseline design and acceptance testing of production elements
  ion source
  RFQ, bunchers, DTLs, spokes and elliptical cavities
  power couplers, tuners, cryo-modules
  RF system including power sources, distribution and controls (LLRF)
200 Accelerating structures and RF distribution points
  minor fault might create a major risk
  must ensure low beam loss operation
    to prevent activation of accelerator components
  major part of the accelerator budget
    must be cost, energy and resource effective for construction & operation
Training of future staff
  participate in prototyping to prepare for operation

## Slide 4: FREIA: RF and Cryogenic Facilities
Test Facility at Uppsala University
  prototyping of LLRF and HLRF solutions
  training of students and staff
4 Years development phase
  2011 – 2012: design, tendering
  2013 – 2014: commissioning, R&D RF systems (components & concepts)
  2015 and beyond: energy efficiency, component testing
Hardware:
  HV pulse modulator
  704 MHz klystron (1.5 MW)
  RF distribution system
  LLRF system
  2 SRF elliptical cavities
  helium liquefier

## Slide 5: Proposals for Possible Test Stand Program
Alternatives HLRF generation and distribution
  prototyping, sufficient contingency in the design
  test alternatives in relation to staging of beam power and energy
  multiple cavities per klystron, min. overhead on possible vector modulator
  multiple klystrons per modulator
Energy efficiency and recovery
  higher efficiency klystrons (long long future)
  energy recovery from klystron/load’s cooling water
Limits in cavity performance
  HOM couplers: multipactoring and use as BPMs
  multi-cavity field emission