## Slide 1: Test Stands
Roger Ruber
Uppsala University
ESS TAC4
16 Feb. 2012

## Slide 2: RF Generation and Distribution System
1 Ion source
~200 RF systems (352 + 704 MHz)
  NC/SC accelerating cavity
  RF source, amplifiers, distribution, controls
Auxillary systems
  5 MW beam → 20 MW mains (losses and overhead)
  Cryo, water and air cooling
Notes: 2

## Slide 3: Objectives for Testing
Validation technical design and performance
  design reliability & contingency: minor fault might create a major risk
  must ensure low beam loss operation to prevent activation
Acceptance testing of production elements
  ion source, accelerating cavities & components: power coupler, tuner
  cryomodules
  RF system: power source, amplifiers, distribution and controls
R&D towards increased operation efficiency and decreased cost
  major part of the accelerator budget
    must be cost, energy and resource effective for construction & operation
Training of future staff
  participate in testing to prepare for operation

## Slide 4: Some Issues to be Addressed
Limits in cavity performance due to field emission
  Comprehensive design studies, prototyping and comprehensive tests of cavities and complete cryomodules
Poor reproducibility in cavity performance
  Quality control during manufacturing and prototyping of a sufficient large number of cavities
Limits in RF system performance and reliability
  Prototyping, sufficient contingency and ease of maintenance in design
Delivery and installation
  Coordinate production and test flow, staging of installation

## Slide 5: Possible Production and Test Flow
Step |  | Industry or Laboratory | Partner Laboratory | ESS Host Laboratory
Accelerator | integration |  |  | 
Cryo-module | acceptance |  |  | 
 | assembly |  |  | 
Components | acceptance |  |  | 
 | manufacture |  |  | 
SRF cavities | acceptance |  |  | 
 | manufacture |  |  | 
 | sub-components |  | procurement | 
Magnets | acceptance |  |  | 
 | manufacture |  |  | 
RF sources | acceptance |  |  | 
 | manufacture |  |  | 

## Slide 6: Overview Prototypes

## Slide 7: Test Stands Overview (not complete)

## Slide 8: Test Stand Matrix

## Slide 9: ESS-UU Collaboration
2009
  ESS has need for R&D and test stand,
    but small staff, no buildings, existing test stands occupied
  start discussion with UU on 704 MHz RF development
  proposal for ESS dedicated test facility at UU
2011
  Spring:
    ESS-UU contract on 704 MHz RF R&D
    ESS changes to 14 Hz rep rate, 2.89 ms beam pulse
  Fall:
    ESS changes pulse modulator strategy → delays UU test stand
2012
  UU starts work on 352 MHz RF for spoke resonators
  keep 704 MHz for future

## Slide 10: Accelerator Physics at Uppsala University
Concentrating on RF and instrumentation …
Cyclotron (since 1948)
CELSIUS ring (1984 – 2006)
CTF3 / CLIC
  Two-beam Test Stand & RF breakdown issues
  FP6-EuroTeV, FP7-EuCARD
  NorduCLIC
FEL
  FLASH Optical Replica Synthesizer,
  XFEL Laser Heater
  Stockholm-Uppsala FEL Centrum
ESS
  ...

## Slide 11: ESS-UU Objectives
Develop 352 MHz RF amplifier for spoke resonators
  validate prototype RF power amplifier
  soak test with prototype LLRF (Lund Univ.) and spoke resonator (IPN Orsay)
Prototype complete RF system and cryomodule
  complete RF system consisting of
    two power amplifiers, RF distribution (Uppsala University)
    LLRF (Lund University)
    cryomodule with two spoke resonators, with tuners (IPN Orsay)
  study high power behaviour, soak test
    Lorenz force detuning, compensation by tuner
    dynamic load, electron emission and multipactoring
    LLRF controls, amplitude and phase stability
Training of future staff
  for acceptance testing and operation

## Slide 12: RF Development Proposal
Contribution to the Technical Design Report (WP8)
  design concept 352 MHz spoke source
  design concept RF distribution
Contribution to the construction planning effort (WP19)
  survey test stand infrastructure and requirements
  study of upgrade scenarios RF systems for ESS power upgrade
Development 352 MHz RF power amplifier for spokes (WP19)
  1st prototype, test with water load and SRF spoke resonator, incl. LLRF
RF system test prototype spoke cryomodule (WP19)
  high power test with 2nd RF power amplifier and LLRF
Acceptance testing spoke cryomodules
  for all final cryomodules before installation
Development klystron pulse modulator
  full test incl. klystron and RF system, if available with SRF cavity

## Slide 13: Projects and Timeline for Coming 5 Years

## Slide 14: FREIA: Accelerator & Instrumentation R&D
New facility at Uppsala University
  cryogenic center (LHe and LN2 distribution)
  RF development project for ESS
  training of students and staff
Integrated with physics and astronomy
  located at Ångström laboratory
  new sub-department (head Tord Ekelöf)
  12 staff (full and part-time)
  multiple funding sources
Hardware
  1000 m2 hall
  helium liquefier (>70 l/h)
  test cryostat
  test bunkers

## Slide 15: FREIA Hall Design

## Slide 16: FREIA Hall Internal Layout
bunkers
RF area
cryo
compressors

## Slide 17: FREIA Cryogenic Infrastructure
Helium liquefier
  100 l/h with LN2 pre-cooling
  2000 l buffer
  distribution box to users
Interfacing
  dewar filling station
    LHe and LN2 dewars
  impure gas recovery from users
  2K pumping station
General purpose test cryostats
  horizontal, like HoBiCat
  vertical

## Slide 18: RF Development Project
352 MHz RF Source development
  352 MHz ~350 kW for ESS double spoke resonators
    possible candidate: TH781
      requires test at 352 MHz and an output cavity development,
      400 kW pulsed should be ok (500 kW pulsed at 200 MHz),
      water cooled
    will study DC or pulsed power supply (energy saving)
  test with water load,
  full RF system test with spoke resonator
Spoke prototype cryomodule testing
  build 2nd RF source
  full RF system test with complete cryo-module prototype
  enables cryomodule acceptance testing for construction phase
Test prototype pulse modulator
  with klystron load

## Slide 19: Conclusions
Uppsala RF development redefined to 352 MHz
  continued contribution to TDR (in WP8)
    RF source for spokes + RF distribution
  prototyping (WP19 ”Test Stands”)
    coordination, survey + RF system upgrade
    soak test spoke source + cryomodule
  proposal to extend with
    acceptance testing spoke cryomodules
    development klystron modulator
Uppsala FREIA project
  engineering for experiment hall in full swing
  negotiations b/w ESS and UU on contract change ongoing
  UU fully commited, promised
    ”taking on such work with priority over work for other possible projects…” (ESS-UU contract agreement)
http://blog.qatestlab.com/2011/04/01/how-to-involve-non-functional-testing-in-your-project/