## Slide 1: LHC dry-runs (BE-BI view)
Should start look seriously at:
  What to test and how (some things are simple, others very much not)
  How to determine ‘success’ ?
    “OK” The screen moved, C.O. position logged, BLM threshold = f(E) inside FPGA !!
  How to document 1) and 2)
  Reasonably ‘light-weight’
  Short dedicated meetings (OP/ABP/ABT/CO/BI) when applicable
Important subjects to not forget:
Full logging deployment (Oracle, SDDS)
  Being looked at presently (meeting next Tuesday)
Full RBAC deployment
  Must be carefully planned (F.E. SW re-link needed)
  CO aims for ‘strict’ policy during 2009
    All applications must authenticate (provide login) for CMW access
    Access maps agreed, deployed and tested (for critical properties)
CMW proxies deployment
  Necessary for certain systems(implications for applications)
  See more during presentation

## Slide 2: Dry-runs 2009 (proposal)
Beam Instrumentation for circulating beam
Ramp
Squeeze
Inject and dump
CIBU tests
Post-mortem

## Slide 3: BI for circulating beam
BPMs (Closed Orbit @1Hz) (feedback service unit)
Interlocked BPMs (Closed Orbit @1Hz)
BLMs (Running Sums @1Hz) (LSA concentrator)
BCTFR (Total + bunch intensities @1Hz)
BCTDC (Total intensity @1Hz)
Tune (Tune ++ @1Hz)
PLL (Tune ++ @1Hz)
Requires only BPNM event (GMT) distributed (automatic)
Goal:
Provide training, ensure tools are available and perform as expected
Date: Anytime (some F.E. may be OFF -> warn us)

## Slide 4: Energy ramp
Use Bruno Puccio’s « Fake Generator » to generate energy ramp to 7 TeV at some realistic rate (repeated on demand)
  Transmit energy information SMP -> GMT -> LHC BST
Use LHC DC BCT systems to transmit (simulated) intensity values:
  BCT 1/2 -> MTT -> SMP -> GMT -> LHC BST 1/2
Would allow testing (BI):
  Safe-beam flag behaviour (interlock masking ON/OFF)
  LHC BLM threshold handling (E)
  Abort-gap system (E + I)
  Luminosity systems (E)
  Wall current monitor (E)
  FFT and PLL excitation amplitude (E)
  BWS SW interlock (E + I)
  BST (1+2) message transmission (E+I)
  Beam feedbacks (function of E)
    Ralph &Jorg dixit: only minor problems expected (!)
    Squeeze discussed next slide
Date: “TBD” (not before 3rd week of March)

## Slide 5: Squeeze (R.S., J.W.)
To be tested before the first squeeze with beam:
  Setting of the reference orbit/bumps via YASP/LSA
  Definition and upload of the squeeze sequence
    Q: Are the complete optics defined/ready in LSA?
    Q: How many optics and how fast are they changed ?
      160 optics in 6 minutes (…)
      50 optics in 20 minutes (tight, but OK)
  Response matrix re-computation on BPM, COD, and optics changes
    Q: How to we change optics:
      Timing event (to be defined) ?
      LHC Sequencer -> FESA property
      Smart operator FB loop?
      Most of pending work depends on the answers
Date: TBD

## Slide 6: Inject and/or dump
BI systems linked to injection:
  BTV (CMW proxies needed)
  BLM (LSA concentrator)
  BPM (LSA concentrator)
  BCTFR (CMW proxies needed)
  Injection related events (+BPM/BLM CAP) tables to be played
  Injection pre-pulses
Date: “TBD”
BI systems linked to beam dump “XPOC”:
  BTV (CMW proxies needed)
  BCTFD
  BLM (LSA concentrator)
  BPMSE, BPMD
  Interlocked BPMs
  XPOC related events table to be played
Date: “TBD”

## Slide 7: CIBU test (BIC)
Bruno Puccio (MPWG) requests low-level software implementation for each front-end connecting to CIBU
BTV, BLM, Interlocked BPM (2009)
Task to be added to LHC sequencer (run before each fill?)
Date: June/July 2009 (lab tests before long)

## Slide 8: Post-mortem
BPM (OK, to be tested)
BLM (OK, to be tested)
Luminosity (OK, to be tested)
BCTDC (implement and test)
BCTFR (implement and test)
BSRT SLOW/FAST (implement and test)
Tune and PLL (implement and test)
Abort Gap (implement and test)
Date: “TBD” (June 2009 proposed)