## Slide 1: Follow-up on tilt of triplet magnets
M. Giovannozzi, R. Tomás
Acknowledgements: A. Herty, H. Mainaud Durand, D. Missiaen

## Slide 2: Recap of situation
Alignment data (tilt angle) of triplet quadrupoles made available in August (ABP-SU):
  Large tilt observed in IR5/8 (up to 0.6 mrad).
Rogelio made the analysis of the impact:
  40% of the coupling observed in IR5 can be explained by the measured tilt.
  10% of the coupling observed in IR8 can be explained by the measured tilt.
A new measurement campaign took place to confirm the results announced in August.

## Slide 5: Summary of tilt measurements
IR1R
IR2
IR5
IR8
IR1L

## Slide 6: Conclusions
Large tilt errors confirmed in recent SU measurement campaign.
IR5 and IR8 feature the largest tilts.
Setting the re-alignment threshold to 0.2 mrad gives the following 7 quadrupoles to re-align:
  Q3L5, Q2L5, Q3R5
  Q2L8, Q1L8, Q1R8, Q2R8
Re-alignment can be performed remotely
This might need to re-check IR bumps and other settings (e.g., injection for IR8).