## Slide 1: S23 optics & polarity checks during injection test 10.08.2008 14:50-19:15
Verena Kain, Mike Lamont,
Laurette Ponce, Rogelio Tomas,
Walter Venturini, Frank Zimmermann,+…

## Slide 2
conditions
low intensity 2x109
further drop during study
initial rf frequency shift -800 Hz kept for
sextupole study ↔ Dp/p ~0.6x10-3 (offset Dp/p~-0.5x10-3 for zero shift!)
help from Walter & Laurette;
rest of team exhausted from aperture study;
numerous interruptions (meeting, low intensity test, BPM crates down, pressure to finish …)
“parasitic” measurements by Brennan et al.

## Slide 3
BPM resolution & orbit stability
x, ~10 minutes
y, ~10 minutes
x,~3 hours
y,~3 hours

## Slide 4: BPM resolution & orbit stability
rms variation of BPM reading
~0.2-0.3 mm over 10 minutes
rms variation of BPM reading
~0.5 mm over 3 hours

## Slide 5: difference orbits w & w/o oscillation
measured y oscillation in arc
may be slightly behind model
measured x oscillation in arc
may be slightly ahead of model
very noisy, but measured x oscillation
may be slightly ahead of model
initial amplitude less than expected?

## Slide 6
difference orbits w & w/o oscillation
~15:00
~17:00
conspicuous pattern repeats!
two sets of data with MCBCV.5R2 taken with 2 hours interval

## Slide 7: inverting model quadrupoles in L3
inverting Q7L3 gives prediction
~consistent with
x measurement
(but not in y; see
next next slides)

## Slide 8
polarity checks
data taken for following S23 circuits:
RSD1&2, RSF1&2, MCS, MSS (slightly off-momentum)
QTL11R2,QTL11L3, QT12R2, QT13R2
QS (no reference orbit)
OD, OF (only one orbit each due to lack of time)
Basic procedure:
launch betatron oscillations with single orbit corrector
change strength or polarity of circuit under investigation, and take four orbits: oscillation for new strength , oscillation for old strength , reference orbit new strength, reference orbit old strength
for sextupole circuits change momentum offset of injected beam

## Slide 9: polarity check Q11L3
measurement with inverted Q11L3 (green dots) is further away from the nominal model (dark blue line)
inverting Q7L3
gives
terrible
result in
y!

## Slide 10: polarity check Q11R2
measurement with inverted Q11R2 (green dots) is closer to nominal model (dark blue line) and vice versa!
polarity error of BPM33.R2.B1?!
conspicuous pattern
reproduced
by QTL11R2
inversion

## Slide 11
polarity check Q12R2
many noisy BPMs but polarity of Q12R2 looks OK

## Slide 12
polarity check Q13R2
many noisy BPMs, polarity of Q13R2 may or may not be OK

## Slide 13
polarity check QS
MQS does not seem to have any effect

## Slide 14: preliminary conclusions
Q11R2 appears to be inverted
BPM.33R2.B1 has wrong polarity
there is another (large) optics error between Q17L3 and Q7L3, in x about equivalent to an inversion of Q7L3 (but this is not it)
MQS has no effect; perhaps not connected?
… data analysis still ongoing