## Slide 1: Timing and synchronisation
Fast timing/synchronisation
  prepulses for SPS extraction and LHC injection with new prepulse system (using warning pulses)
  prepulses for BI (21 turns before injection) stable
  some GMT timing issues...
RF frequency control & rephasing
  change LHC reference frequency (temporarily Agilent generator)
  SPS rephasing follows correctly
  some bugs ironed out in the rephasing system
  frequency range +/- 800Hz @ 400 MHz will be increased by factor 2
  rephasing error signal will be made permanently available in OASIS

## Slide 2: RF synchro bucket/ring selection
Injection request specifies next injection ring/bucket
Next injection ring/bucket sent as payloads of timing events HX.RGNI and HX.BKNI
Used by LHC RF synchro equipment to reconfigure fc and LHC injection pulse generator delays. Injector chain follows.
HX.RGNI and HX.BKNI need to arrive 450ms before PS-SPS transfer
BUT: injection request mechanism in CBCM means they are sent only at start of SPS LHCFAST cycle
“Quick fix” found using sequencer. Julian proposes more definitive solution. To be discussed...
fc

## Slide 3: Rephasing error signal